PulseBusta - S

for the

Range Rover Sport

and

Discovery 3

PulseBusta will stop a trailer’s turn signal LEDs from blinking and provide trailer recognition

# PulseBusta-S-B 						       PulseBusta-S-C

The B version is supplied pre-wired with 		   	     The C version is mounted on your trailer.

about 600mm (2ft) of 7-core cable for you	   	    Any vehicle can tow a trailer with a PulseBusta-C fitted

to fit your own connectors.     			       as its operation is transparent to the towing vehicle.

Order Code: Busta-S-B - $    	 	GST, Pack & Post included	 Order Code: Busta-S-C - $

The PulseBusta-S does not monitor the trailer turn signal LEDs and is therefore unable to inform the driver if a fault is present.  The onus is on the driver to check that all of the trailers LEDs are functioning correctly.   PulseBusta-E is under development and will monitor the trailer’s turn signal LEDs.  Please check which model you require before ordering.

It is quite normal for a PulseBusta to get very WARM when the turn signals have been used and it can even get quite HOT when the hazards have been in operation.  PulseBusta is manufactured with high temperature – long life components as it contains two dummy load resistors and it is these that get hot when the turn signals or hazards are in operation.

PulseBusta cannot be fitted to the vehicle, as it will always recognise that a trailer is connected.

(Refer to Safety Alert)

# Patented in Australia #2006200462, UK #GB2440603

# Please pay by cheque, postal money order or PayPal (Please add 3% when paying by PayPal).

Pay Pal payments use labtronx@bigpond.com

You may also pay by direct credit to:

# Berrima District Credit Union Ltd

411 Bong Bong Street, Bowral NSW 2576

BSB: 802101

LAB Electronics Pty Ltd

Account No 350629

Please use your name and the Order Code as the Lodgement reference.

Then send us an e-mail informing us:

1. That you have made the payment.

2. What you have ordered.

3. Your name, postal delivery address and phone number.

## Towing with a Range Rover Sport or Discovery 3

All Range Rover Sport and Discovery 3 owners, trailer manufacturers, trailer retailers, and trailer hire companies are at risk due to the known issues that exist when trailers with LED turn signals are being towed with the above Land Rover vehicles.

For both legal and safety reasons a trailer cannot be towed with its turn signal LEDs continuously blinking and the vehicle’s Body Computer must recognise that a trailer is connected.

PulseBusta stops both park and the turn signal LEDs from blinking continuously while also enabling and disabling various vehicle functions (trailer recognition).

The Air Suspension is programmed to automatically lower the ride height by approximately 20mm at highway speeds to improve the vehicle’s handling characteristics.  The Air Suspension will also automatically return to standard ride height to when the vehicle slows.  These ride height changing actions must be disabled when towing to prevent the possibility of introducing directional instability at high speed.

The Anti-Lock Brake, Stability and Traction Control systems can employ different strategies in controlling the vehicle dynamics when towing a trailer.

The Power Train Control systems can employ different strategies when towing a trailer by altering the automatic transmission shift points and providing enhanced dynamic engine braking.

The trailer telltale lamp in the vehicle’s instrument cluster must be enabled, as this is a legal requirement in most markets.

Rear fog and reversing lights (when they would normally be illuminated) are disabled on the vehicle to eliminate the forward reflections of those lights from the front of the trailer affecting the driver’s vision.

# Rear parking sensors are disabled.

PulseBusta must be fitted to the trailer. It cannot be fitted to the vehicle, as the vehicle will always recognise that a trailer is connected and the above trailer connected functions will occur.

# Text boxes

Contact:   Lee Bourgeois

Phone - after 10:30 am M, W & F

(02) 4871 1218

e-mail:  mail@labtronx.com.au

www.labtronx.com.au

Safety alert

Contact:   Lee Bourgeois

Phone - after 10:30 am M, W & F

(02) 4871 1218

e-mail:  mail@labtronx.com.au

www.labtronx.com.au

LAB Electronics Pty Ltd

13 Oxford Street

Mittagong NSW 2575

AUSTRALIA

LAB Electronics Pty Ltd

13 Oxford Street

Mittagong NSW 2575

AUSTRALIA